## Slide 1
Technical Specifications
Cairo Tower LED Mesh Display System

## Slide 2
LED Mesh Display System
• Total Area: 3,300 m² (35,520 ft²)
• Pixel Pitch: P16 (16mm spacing)
• Brightness: 6,000 nits ( daylight visible)
• Transparency: 50% light transmission
• Weather Rating: IP68 (waterproof)
• Operating Temp: -20°C to +60°C

## Slide 3
LED Technology
• Module Type: Transparent LED mesh panels
• Color Depth: Full RGB, 16.7 million colors
• Refresh Rate: 3,840 Hz (no flicker)
• Viewing Angle: 140° horizontal/vertical
• Lifespan: 100,000 hours (11+ years)
• Energy Consumption: ≤800W per m² average

## Slide 4
Display Architecture
Panel Configuration
• Modular 500x1000mm panels
• Seamless edge-to-edge display
• Curved surface adaptation
• Redundant power modules
• Hot-swappable components
• Remote monitoring enabled
Structural Integration
• Minimal impact on tower aesthetics
• Wind load engineered design
• Safety factors built-in
• Cable management concealed
• Anti-vibration mounting
• Access for maintenance

## Slide 5
NovaStar 4K Control System
• Processing: NovaStar MCTRL4K
• Video Inputs: 4x 4K @60Hz
• Output: 16x Gigabit Ethernet ports
• Color Depth: 16-bit processing
• HDR Support: Yes (HDR10/HLG)
• Refresh Rate: Up to 3840Hz

## Slide 6
Network & Connectivity
• Primary: Fiber optic connection
• Backup: Secondary fiber link
• Protocol: sRGB, HDR support
• Latency: <16ms end-to-end
• Remote Access: VPN secured
• Content Sync: Real-time cloud

## Slide 7
Creative Production Studio
Hardware
• 2x Production Workstations
• 96TB NAS Storage Array
• 4K Reference Monitors
• Rendering Farm (50 cores)
• Audio Production Suite
• VR Development Station
Software
• Adobe Creative Cloud
• Cinema 4D (3D rendering)
• Houdini (VFX)
• After Effects (Compositing)
• DaVinci Resolve (Editing)
• TouchDesigner (Interactive)

## Slide 8
Interactive Experience Systems
• VR Cinema: 8-seat immersive theater
• AR Photo Booths: 4 stations
• Panoramic Flight Sim: 360° experience
• Gesture Control: Motion detection
• Holographic Display: 3D projections
• Touch Kiosks: Information & booking

## Slide 9
Power & Electrical
• Total Power: 2.64 MW peak
• Supply: 3-phase industrial
• UPS Backup: 30 minutes
• Generator: 3MW capacity
• Power Factor: 0.95+
• Monitoring: Real-time meters

## Slide 10
Environmental Specifications
• Wind Load: 240 km/h rated
• Seismic: Zone 2 compliant
• Lightning: Full grounding system
• EMI/RFI: Shielded design
• Noise Level: <65dB at 1m
• Fire Rating: Class B1 materials

## Slide 11
Maintenance & Support
• Remote Diagnostics: 24/7 monitoring
• Preventive Maintenance: Monthly
• Panel Replacement: <4 hours
• Software Updates: Quarterly
• Spare Parts: 5% inventory on-site
• Warranty: 5-year comprehensive

## Slide 12
Key Specifications Summary
Chart: 
| Resolution (Mpx) | Pixel Density | Brightness (nits) | Refresh (Hz) | View Angle
Value | 26 | 3906 | 6000 | 3840 | 140

## Slide 13
Thank You
Cairo Tower LED Technical Specifications